## Slide 1
Mikhail Shalaginov
PHYS 522
Nitrogen-vacancy center in diamond
as a true gift of nature

## Slide 2: Evolution of information society
Information Storage: 1986 - 0.5 GB per person
2007 - 44.5 GB per person
Information Transmission: 1986 - 0.281 EB
2007 - 65 EB
Computation: 1986 - 0.3G MIPS
2007 - 6400G MIPS
M. Hilbert and P. López,Science , 332(6025), 60–65 (2011)
Notes: We live in the age, where the information is playing extremely important role, in particular, its storage, transmission, and computation. I would like to draw your attention to the following facts. For example, in 1986 the world’s technological capacity to store information was about 500 MB per person, which is equivalent to the capacity of one CD, and in 2007 it grew to 44.5 GB per person, the same as 60 CDs per person. If we consider the world’s effective capacity to exchange information through two way telecommunication networks, for the same period of time it increased more than 200 times from 0.2 to 65 exabytes. One exabyte is a billion of gigabytes. The world’s technological capacity to compute information with human guided general-purpose computers grew more than 20,000 times in 20 years.
Nowadays the discussed parameters are expected to be substantially higher and continue to rise. It is good to know that information society is rapidly developing; however, this also brings some technological problems with providing fast and efficient access to information.

## Slide 3: Promising ways of IT evolution
Optical computing
Quantum computing
Spintronics
DNA computing
Artificial intelligence
Notes: Unfortunately, current technologies based on electronics are reaching its limit and scientists are looking for new approaches. Here you can see some of the directions, among them is optical and quantum computing. Development of quantum computing is important because most of the information is transferred through optical fibers but transmitters and receivers are based on electronics. As a result, much time is lost on conversion processes. If it were all based on photonics it could work much faster. Quantum computing is interesting because of its algorithms which can solve problems much faster than classical ones. In addition, quantum nature of computation provides us with such things as entanglement which allows information teleportation. Moreover, cryptography based on quantum principles can safeguard the transferred information at the highest available level of security.

## Slide 4: Storage of quantum information
Superconducting resonators and Josephson junctions
SiGe gate-defined spin qubits
Majorana fermions in superconductor/semiconductor nanowire hybrid materials
Spin defects in solids
Hyperfine states in trapped ion systems
J. N. Eckstein & J. Levy, MRS Bulletin (2013)

## Slide 5: Transmission of quantum information: single photon sources
Single terrylene molecules
in a p-terphenyl crystal
B. Lounis, et al, Nature (2000)
CdSe/ZnSe Quantum Dots
X. Wang, et al, Nature (2009)
Trapped Ba Ions
courtesy of B. Blinov, University of Washington (2011)
NV Color Centers
F. Jelezko, et al, Phys. Status Solidi A (2006)

## Slide 6: Questions to uncover about NV centers
General facts and a little bit of history
Electronic level structure
Distinct properties
Applications
My research in this area

## Slide 7: General facts about NV center
Historical facts
More than 50 years of NV research:
In 1997 J. Wrachtrup et al: photostability room temperature operation, optically detected magnetic resonance
How to create it
Naturally can be found in diamond crystals (N most common impurity)
Artificially created by ion/electron irradiation and subsequent annealing
Jorg Wrachtrup
Notes: in 1997.[7] In that paper, it was demonstrated that the fluorescence of single N-V− centers can be detected by room-temperature fluorescence microscopy and that the defect shows perfect photostability. Also one of the outstanding properties of the NV center was demonstrated, namely room-temperature optically detected magnetic resonance.
Institute of Physics, University of Technology Chemnitz,
Reichenhainer Strasse 70, 09126 Chemnitz, Germany
annealing at temperatures above 700 0C

## Slide 8: Electronic structure of NV- center
D.D. Awschalom , et al, PNAS ( 2010 )
Notes: Figure 1. Schematic representation of the electronic structure of a point defect in a
tetrahedrally coordinated elemental semiconductor such as diamond. (a) The electronic
states corresponding to the sp 3 orbitals on an isolated C atom. (b) The superposition
of these orbitals that gives rise to the band structure of an infi nite solid. The overlap
of orbitals leads to bonding and antibonding states, which broaden into valence and
conduction bands. If a carbon atom is removed, as shown in (c), a vacancy is created,
and the four orbitals on the surrounding atoms interact with each other in the tetrahedral
environment to give rise to states with a 1 and t 2 symmetry. Because the interaction between
these orbitals is weaker than the C-C interaction that gives rise to the bands in the solid, the
defect-related electronic states lie within the bandgap of the semiconductor. A symmetrylowering
perturbation, such as incorporation of a nitrogen atom on one of the sites around
the vacancy (d), further splits the t 2 states. Adapted from Reference 16.

## Slide 9: Electronic structure of NV- center
Optical initialization
Spin-dependent fluorescence
Switching between spin-states by using microwave signal

## Slide 10: Single-shot readout (SSR) technique
P. Neumann, et al, “Single-shot readout of a single nuclear spin.,” Science, vol. 329, no. 5991, pp. 542–4, 2010.

## Slide 11: Broad emission spectrum of NV center
J. Wrachtrup, phys. stat. sol. (a) 206
wikipedia

## Slide 12: Applications of NV centers
Quantum bits/registers
Quantum photonic networks
Nanoscale sensors of electric and magnetic field
Nanoscale thermometer
Biomarking

## Slide 13: Optical &quantum computer technologies based on NV centers
NV center as a single-photon source:
photostable
operates as single-photon source
at room temperature,
broadband emission spectrum
NV center as a quantum memory unit:
long electron-spin coherence time
can be optically read out
nitrogen-vacancy (NV)
color center in diamond
Effeciency of NV center as a component of quantum computers and networks
is directly related to its optical emission rate!
Jelezko, Wrachtrup, Phys. Status Solidi A (2006)
Kurtsiefer, et al, Phys. Rev. Lett. (2000)
Maurer, et al, Science (2012)
Notes: The most promising candidate to become a component of optical quantum computer is a nitrogen-vacancy center (or NV center). First, it can be used as a source of single photons, because it is photostable, works at room temperatures. In addition, its emission spectrum is relatively broad, which enables multichannel signal transfer. Second, NV-center can serve as a quantum memory unit based on electron spin. An NV-center can stay in a state with the same value of spin for a rather long period of time, which is about millisecond and the state can be read out optically. Effectiveness of a NV center as a single photon source and as a quantum memory unit is directly related to its optical emission rate.

## Slide 14: Ways to enhance emission efficiency
diamond-silver apertures
J. T. Choy, Nat. Photon. 2011
diamond microring resonator
A. Faraon, Nat. Photon. 2011
photonic crystal cavity
A. Faraon, PRL 2012
gold nanoparticles
S. Schietinger, Nano Lett. 2009
Notes: According to Fermi’s golden rule, the radiative decay rate depends on both the internal properties of an emitter and the density of electromagnetic modes in the environment. Therefore, engineering the light source environment (Purcell effect) can lead to improvement of the spontaneous emission rate. So far, this idea has been implemented with resonant structures, such as optical resonators, photonic crystal cavities, and plasmonic apertures, which are all bandwidth-limited. In this work, we experimentally study non-resonant broadband enhancement of the emission from NV centers coupled with hyperbolic metamaterials (HMMs).
-diamond-silver apertures: nanoposts (radius 50nm, height 180 nm, manufactured in single-crystal diamond by reactive ion etching) from previous Loncar’s work covered with silver layer to create plasmonic cavities.
-gold nanoparticles: plasmon-enhanced single-photon emission, on the picture depicted AFM images of a single diamond
nanocrystal (left), to which one (middle) or two (right) gold nanoparticles are coupled.
-diamond microring resonator: coupling of the zero-phonon line of individual nitrogen vacancies to the modes of microring resonators fabricated in single-crystal diamond.
-photonic crystal cavity: zero-phonon transition rate of a nitrogen-vacancy center is enhanced by coupling to a photonic crystal resonator fabricated in monocrystalline diamond using standard semiconductor fabrication techniques.

## Slide 15: Hyperbolic metamaterials & broadband Purcell effect
Z. Jacob, et al, Appl Phys B, (2010)
H. N. S. Krishnamoorthy, et al, Science (2012).
O. Kidwai, et al, Phys. Rev. A (2012)
M. A. Noginov, et al Opt. Lett. (2010).
Notes: Our approach takes advantage of the large photonic density of states (PDOS) in a broad range of wavelengths, which is a striking property of HMMs. The PDOS, similar to its electronic counterpart, can be quantified as the volume in k-space between isofrequency surfaces. For extraordinary waves in a uniaxial anisotropic medium with dielectric tensor, iso-frequency surfaces are defined by the following dispersion relation formula. In case of conventional materials, PDOS is equivalent to an infinitesimally thin ellipsoidal shell in k-space. However, in a medium with hyperbolic dispersion hyperboloid shell appears whose volume is infinitely large in the effective medium limit (i.e. broadband singularity in PDOS appears). As a result, such a medium allows the propagation of spatial modes with an arbitrarily large wave vectors. However, in real structures, the maximum value of the wave vector is restricted by the size of the metamaterial unit cell (which is much smaller than the wavelength in a metamaterial).

## Slide 16
M. Y. Shalaginov1,2, V. V. Vorobyov3,4, J. Liu5,
J. Irudayaraj5, A. V. Akimov4,6,7, A. Lagutchev2, A. V. Kildishev1,2,
and V. M. Shalaev1,2
1School of Electrical and Computer Engineering, Purdue University, West Lafayette, USA
2Birck Nanotechnology Center, Purdue University, West Lafayette, USA
3Photonic Nano-Meta Technologies, Moscow Region, Mytischi, Olimpijskij Prospekt 2, 141009 Russia
4Moscow Institute of Physics and Technology, 9 Institutskiy per., Dolgoprudny, Moscow Region, 141700, Russia
5Agricultural and Biological Engineering, Purdue University, West Lafayette, USA
6Russian Quantum Center, Novaya str., 100, BC "Ural", Skolkovo, Moscow region, 143025, Russia
7Lebedev Physical Institute RAS, 53 Leninskij Prospekt, Moscow, 119991, Russia
Single-photon source based on
NV center in nanodiamond
coupled to hyperbolic metamaterial

## Slide 17: Milestones
“Characterization of nanodiamonds for metamaterial applications” (Applied Physics B 105.2 (2011): 191-195)
“Broadband enhancement of spontaneous emission from nitrogen-vacancy centers in nanodiamonds by hyperbolic metamaterials” (Applied Physics Letters 102.17 (2013): 173114)
“Towards single-photon source based on NV center in nanodiamond coupled to CMOS-compatible hyperbolic metamaterial” (to be submitted)
“Effect of planar hyperbolic metamaterial on radiation pattern of single-photon source” (to be submitted)

## Slide 18: Experimental set-up
Hanbury Brown-Twiss interferometry
Time –correlated single photon counting

## Slide 19: Broadband enhancement of spontaneous emission from NV centers in nanodiamonds by HMMs
radiative decay increased 2.5 times in comparison to glass surface (total decay rate is increased 13.5 times).

## Slide 20: Towards single-photon source based on NV center in nanodiamond coupled to CMOS-compatible hyperbolic metamaterial
Al0.7Sc0.3N
TiN
2 nm
1st epitaxial single crystalline metal/semiconductor superlattice G. Naik, et al, PNAS (2014)
Photon anti-bunching statistics

## Slide 21: Effect of planar hyperbolic metamaterial on radiation pattern of single-photon source
radiation pattern becomes more narrower directed and collected emission power for the single dipole emitter (averaged over its all polarizations) located on top of TiN-based HMM is increased about 2

## Slide 22: Conclusions
Observed decrease in lifetime and enhancement in registered emission rate from NV centers on top of multilayer HMMs
Future work
To develop methods of efficient outcoupling of high-k modes